## Slide 1
NSO Local Setup
- Shankar S. Warudkar

## Slide 2
NSO
Device Management
Agenda
NSO Local Installation
Onboarding Devices into NSO
Device Management
NSO Northbound API

## Slide 3
Installing NSO and NED
Download NSO Installation Files and tools
Ready Your Server with Pre-requisites
Perform NSO Local installation
How to Login NSO cli and webUI
Perform NED installation
Netsim
Using Netsim to create Devices
Add more devices to netsim Network with defferent neds
Device Onboarding in NSO
Device onboarding MOP
Device onboarding using ncs cli and Webui
Device onboarding in NSO using rest API
Device config management
Using ncs cli
Using webui
Using nso Northbound api
Topics

## Slide 4
NSO 5.1.2
NSO Installation bin file
nso-5.1.2.linux.x86_64.signed.bin
NEDs
ncs-5.1.2-cisco-ios-6.41.signed.bin
ncs-5.1.2-cisco-iosxr-7.17.signed.bin
ncs-5.1.2-juniper-junos-4.5.17.signed.bin
Toolkit
Vbox or VmWare
Ubuntu 18.04 iso image
Winscp
Putty
Postman
Network Simulator (Optional)
Download NSO Installation Files and tools

## Slide 5
Enable ssh after OS installation
sudo apt update
apt install net-tools
apt install openssh-server
apt install ssh
systemctl status ssh
ufw allow ssh
Confirm SSH Connection
Test Locally
ssh username@localhost
Remote ssh
ssh username@nso_server_ip
Confirm scp from remote pc
For Local Lab Setup
VBox settings to
Communicate Guest OS to HOST PC
Use Adapter – host only adapter
NAT
File Transfer using FTP Tool
ftp
nso bin file
ned bin file
Install NSO dependencies
apt install default-jre
apt install ant
apt install python3.7
apt install build-essential
apt install default-jdk
Pre-requisites

## Slide 6
Check your $HOME directory
root@nso-VirtualBox:/home/nso/Downloads# $HOME
bash: /root: Is a directory
### NSO Install – Go to your file download dir
$sh nso-5.1.2.linux.x86_64.signed.bin --skip-verification
$ mkdir ~/nso-(nsoversion)
$sh nso-5.1.2.linux.x86_64.installer.bin --local-install ~/nso- 5.1
$cd ~/nso-5.1
$source $HOME/nso-5.1/ncsrc
Check Environment Variable
root@nso-VirtualBox:~/ncs-run# env | grep NCS_DIR
NCS_DIR=/root/nso-5.1
root@nso-VirtualBox:~/ncs-run# env | grep HOME
HOME=/root
$ncs-setup --dest $HOME/ncs-run
$cd ~/ncs-run
root@nso-VirtualBox:~/ncs-run# ncs
root@nso-VirtualBox:~/ncs-run# ncs_cli -C -u admin
admin connected from 127.0.0.1 using console on nso-VirtualBox
admin@ncs#
NSO INSTALLATION

## Slide 7
Login to nso
ssh nso@192.168.56.108
nso@192.168.56.108's password:
nso@nso-VirtualBox:~$ sudo su
[sudo] password for nso:
root@nso-VirtualBox:/home/nso#
root@nso-VirtualBox:/home/nso# ~/
bash: /root/: Is a directory
root@nso-VirtualBox:/home/nso# source ~/nso-5.1/ncsrc
root@nso-VirtualBox:/home/nso# cd ~/ncs-run/
root@nso-VirtualBox:~/ncs-run# ncs
root@nso-VirtualBox:~/ncs-run# ncs --status | grep status
status: started
db=running id=33 priority=1 path=/ncs:devices/device/live-status-protocol/device-type
root@nso-VirtualBox:~/ncs-run# ncs_cli -C -u admin
admin connected from 127.0.0.1 using console on nso-VirtualBox
admin@ncs#
Check NSO Webui Access
http://nso_ipaddress:8080/
http://192.168.56.108:8080
Credentials : admin/admin
How to start ncs

## Slide 8
root@Labpc:~/ncs-run/packages# sh ncs-5.1.2-cisco-ios-6.41.signed.bin --skip-verification
Unpacking...
root@Labpc:~/ncs-run/packages# ls
cisco_x509_verify_release.py ncs-5.1.2-cisco-ios-6.41.tar.gz README.signature
ncs-5.1.2-cisco-ios-6.41.signed.bin ncs-5.1.2-cisco-ios-6.41.tar.gz.signature tailf.cer
cd ~/ncs-run/packages
root@nso-VirtualBox:~/ncs-run/packages# cp -r /home/nso/Downloads/IOSXE/ncs-5.1.2-cisco-ios-6.77.12.tar.gz ncs-5.1.2-cisco-ios-6.77.12.tar.gz
root@nso-VirtualBox:~/ncs-run/packages# l
ncs-5.1.2-cisco-ios-6.77.12.tar.gz
root@nso-VirtualBox:~/ncs-run/packages# ls -ltrh
total 55M
-rw-r--r-- 1 root root 55M May 7 16:25 ncs-5.1.2-cisco-ios-6.77.12.tar.gz
root@nso-VirtualBox:~/ncs-run/packages#
root@nso-VirtualBox:~/ncs-run/packages# cd ..
root@nso-VirtualBox:~/ncs-run# ncs_cli -C -u admin
admin@ncs# packages reload
……
>>> System upgrade has completed successfully.
reload-result {
package cisco-ios-cli-6.77
result true
}
admin@ncs#
System message at 2022-05-07 16:27:08...
Subsystem started: ncs-dp-1-cisco-ios-cli-6.77:IOSDp
admin@ncs# show packages package package-version
PACKAGE
NAME VERSION
-----------------------------
cisco-ios-cli-6.77 6.77.12
admin@ncs#
admin@ncs#
NED Installation

## Slide 9
admin@ncs# show packages package oper-status
PACKAGE
PROGRAM META FILE
CODE JAVA BAD NCS PACKAGE PACKAGE CIRCULAR DATA LOAD ERROR
NAME UP ERROR UNINITIALIZED VERSION NAME VERSION DEPENDENCY ERROR ERROR INFO
----------------------------------------------------------------------------------------------------------------
cisco-iosxr-cli-7.17 X - - - - - - - - -
admin@ncs# show packages package package-version
PACKAGE
NAME VERSION
-------------------------------
cisco-iosxr-cli-7.17 7.17
admin@ncs#

## Slide 10
Create non-default authgroup to authenticate the devices
admin@ncs(config)#
devices authgroups group asriosxe
umap admin remote-name cisco remote-password cisco123
TEST11
ncs_cli –C –u admin
config
devices device TEST11
address 127.0.0.1 port 10023
device-type cli ned-id cisco-ios-cli-6.77 protocol ssh
authgroup default
state admin-state unlocked
commit
ssh fetch-host-keys
sync-from
check-sync
NOTE:You may require to change the device global setting for ssh authentication with real devices or Virl or virtual routers.
admin@ncs(config)# show full-configuration devices global-settings ssh-algorithms
devices global-settings ssh-algorithms public-key [ ssh-rsa ]
If below issue came:
admin@ncs(config-device-CSRKV-1)# ssh fetch-host-keys
result failed
info Failed to authenticate towards device CSRKV-1: SSH key exchange failed
admin@ncs(config-device-CSRKV-1)#
While enabling ssh on cisco device we use rsa crypto key
Adding Devices in NSO using ncs cli

## Slide 11
Cisco IOS/IOS-XE Router config to enble ssh enable access
CSRKV-1
Sample config
hostname CSRKV-1
ip domain name cisco.com
username cisco privilege 15 secret 5 anypassword
ip ssh version 2
line vty 0 4
login local
transport input ssh
crypto key generate rsa
ip ssh time-out 120
ip ssh version 1
Configure at least one inteface which should be reachable from your nso server
interface GigabitEthernet1
ip address 192.168.56.60 255.255.255.0
negotiation auto
What if you are choosing router device from ncs-netsim devices to onboard in NSO.
You choose to pick real device or cisco VIRL or cisco ASR 1000asr vm image. - Enabling ssh at the device first. - Production devices will be come ready with ssh access. You may not need to configure ssh access at router.

## Slide 12
Using simulator devices in absence of real devices for lab purpose
Netsim feature come by default with nso installation .
Create netsim devices
ncs-netsim create-network packages/ncs-5.1.2-cisco-ios-6.77.12.tar.gz 3 TEST1
3 – number of devices to create
TEST1 – prefix name for devices
root@nso-VirtualBox:~/ncs-run# ncs-netsim create-network packages/ncs-5.1.2-cisco-ios-6.77.12.tar.gz 3 TEST1
DEVICE TEST10 CREATED
DEVICE TEST11 CREATED
DEVICE TEST12 CREATED
root@nso-VirtualBox:~/ncs-run# ncs-netsim start
DEVICE TEST10 OK STARTED
ncs-netsim is-alive
ncs-netsim --help
root@nso-VirtualBox:~/ncs-run# ncs-netsim list
ncs-netsim list for /root/ncs-run/netsim
name=TEST10 netconf=12022 snmp=11022 ipc=5010 cli=10022 dir=/root/ncs-run/netsim/TEST1/TEST10
name=TEST11 netconf=12023 snmp=11023 ipc=5011 cli=10023 dir=/root/ncs-run/netsim/TEST1/TEST11
name=TEST12 netconf=12024 snmp=11024 ipc=5012 cli=10024 dir=/root/ncs-run/netsim/TEST1/TEST12
root@nso-VirtualBox:~/ncs-run#
NCS NETSIM Device Setup

## Slide 13
TEST11
root@nso-VirtualBox:~/ncs-run# ncs-netsim cli-c TEST11
admin connected from 127.0.0.1 using console on nso-VirtualBox
TEST11# show running-config
root@nso-VirtualBox:~/ncs-run# ncs-netsim add-to-network packages/ncs-5.1.2-cisco-iosxr-7.38.5.tar.gz 2 PRODXR10
DEVICE PRODXR100 CREATED
DEVICE PRODXR101 CREATED
name=PRODXR100 netconf=12025 snmp=11025 ipc=5013 cli=10025 dir=/root/ncs-run/netsim/PRODXR10/PRODXR100
name=PRODXR101 netconf=12026 snmp=11026 ipc=5014 cli=10026 dir=/root/ncs-run/netsim/PRODXR10/PRODXR101
Login to netsim devices
ADD More devices to netsim network with different or same NED

## Slide 14
NSO device Config Management
devices device check-sync
sync-from
connect
ping
compare-config
commit actions
commit dry run
Commit no-networking